## Slide 1
WEEKLY-REPORT
Ho Chi Minh City University of Technology
Faculty of Transportation Engineering
Student name’s: Nguyen Quoc Kiet
ID: 1952802

## Slide 2
CONTENT
01
02
03
06
07
INTRODUCTION
THEORETICAL BASIS
GENERAL LAYOUT DESIGN
TIMING DIAGRAM
SIMULATION AND RESULTS
ALGORITHMS
04
WIRING DIAGRAM
05

## Slide 3
INTRODUCTION
  This report will show the measuring product design and the method how to measure the alternator’s speed.
  Using Arduino Uno to measure the single phase’s frequency then calculate the alternator’s RPM
  Testing in room temperature 25(Degrees); no shock or vibration; test in short time (< 30 minutes)
  Measuring range: 500 – 8500 RPM
  Error ≤ 5%

## Slide 4
THEORETICAL BASIS
  The alternator is a 3-phase synchronous generator
  Phase voltage: is the voltage measured across a single
component in a three-phase source or load
  General Information

## Slide 5
THEORETICAL BASIS
2. The relationship between alternator’s speed and frequency
Frequency = 1 / Time period
P: number of pair poles
n: alternator of speed

## Slide 6
THEORETICAL BASIS
2. The relationship between alternator’s speed and frequency
Figure: Frequency of 3-phase (AC) voltage

## Slide 7
THEORETICAL BASIS
2. The relationship between alternator’s speed and frequency
Figure: Single phase voltage signal after rectifier

## Slide 8
THEORETICAL BASIS
2. The relationship between alternator’s speed and frequency
Figure: Frequency of one phase voltage with respect ground

## Slide 9
THEORETICAL BASIS
2. The relationship between alternator’s speed and frequency
Figure: Frequency of one phase voltage after Schmitt Trigger

## Slide 10
Using signal conditioning to convert input signals (sine waves) into digital signals (square waves).
Using microcontroller to measuring the frequency from the converted signals.
Display the results.
THEORETICAL BASIS
3. Measuring method:
METHOD

## Slide 11
GENERAL LAYOUT DESIGN

## Slide 12
Figure 3. V diagram
DC motor dynamometer: control and measuring system
Objectives & technical requirements
General layout design
Measurements testing, controllers testing
Conclusion
Characteristic curve drawing and evaluation
Technical design: measurements, controllers, GUI

## Slide 13
WIRING DIAGRAM

## Slide 14
TIMING DIAGRAM
Where:
: the period of Alternator signal.
the frequency of Alternator signal
clock speed of Arduino ( )
Prescaler: frequency divider (= 64)
the frequency of Timer/Counter 1.
ICR1: The ICR1 register will “capture” the value of the Timer/Counter1
counter register.
TOP: the peak value at which the Timer/Counter1 changes state.
BOTTOM: the lowest value that a Timer/Counter 1 reaches.
: count value of Timer/Counter1 that counted from to .
n: number of overflow.
at the falling edge of the speed signal.
at the next falling edge of the speed signal
: count value of Timer/Counter 1 at .
: count value of Timer/Counter1 at .
P: number of pair poles
At : Jump to interrupt program of the falling edge: and set n = 0.
After, exit interrupt program and the program continues execution. Until Timer/Counter1 overflow, jump to interrupt program Overflow and n++ ( if n>1  n =0 )
At : Jump to interrupt program of the next falling edge:
and after that, save , then calculate the value of  Calculate f 
Calculate S  Serial display (Delay 1000ms)
Reset: When n != 0  , n = 0
n = 0  (ko update)
Continues program, at : Save . Save .
Then, Calculate value of
Reset: When n != 0  , n = 0
n = 0  (ko update)

## Slide 15
TIMING DIAGRAM
Where:
: the period of Alternator signal.
the frequency of Alternator signal
clock speed of Arduino ( )
Prescaler: frequency divider (= 64)
the frequency of Timer/Counter 1.
ICR1: The ICR1 register will “capture” the value of the Timer/Counter1
counter register.
TOP: the peak value at which the Timer/Counter1 changes state.
BOTTOM: the lowest value that a Timer/Counter 1 reaches.
: count value of Timer/Counter1 that counted from to .
n: number of overflow.
at the falling edge of the speed signal.
at the next falling edge of the speed signal
: count value of Timer/Counter 1 at .
: count value of Timer/Counter1 at .
P: number of pair poles
At : Jump to interrupt program of the falling edge: and set n = 0.
After, exit interrupt program and the program continues execution. Until Timer/Counter1 overflow, jump to interrupt program Overflow and n++ ( if n>1  n =0 )
At : Jump to interrupt program of the next falling edge:
and after that, save , then calculate the value of  Calculate f 
Calculate S  Serial display (Delay 1000ms)
Reset: When n != 0  , n = 0
n = 0  (ko update)
Continues program, at : Save . Save .
Then, Calculate value of
Reset: When n != 0  , n = 0
n = 0  (ko update)

## Slide 16
n++ 0,5s read a result one time T_overflow = 10 ms,
overflow= 2500 Display_flag = 1
Print: ; ; overflow_count; Frequency (f), Speed (S) Display_plag = 0
Calculate_flag = 0
;
Calculate_flag = 1
Display_flag = 1
Calculate_flag = 1
Send data
Send data
Void Loop ()
Overflow interrupt
Falling edge interrupt
Display program
Calculate speed program
Save data to global variable
WORK-FLOWS

## Slide 17
ALGORITHMS
the cycle of Alternator signal
clock speed of Arduino ( )
P: number of pair poles
: count value of T/C1 that counted from to .
: is count value of T/C1 at the falling edge of the speed signal.
: is count value of T/C1 at the next falling edge of the speed signal.
n: number of overflow.
S: Alternator speed (RPM)
TOV1: T/C1 Overflow flag
ICF1: T/C1 Input capture flag
ICR1: The value of the ICR1 register will be updated according to the TCNT1 register each time an interrupt occurs.

## Slide 18
Main program
Reset all register;
Set prescaler Enable input capture interrupt Enable overflow interrupt
TOV1 = 1
ICF1 = 1
ISR(TIMER1_OVF_vect)
Display_flag = 1
ISR(TIMER1_CAPT_vect)
Calculate_flag = 0
Serial display Display_flag = 0
Return
TRUE
TRUE
FALSE
FALSE

## Slide 19
SIMULATION AND RESULTS
Fixed Frequency case:
F: Input Frequency (Hz).
(RPM), P = 3: number of pole pairs
: measured frequency in fixed case
(RPM)
: error when measuring in fixed case
Input frequency/Input Speed (F/S) | Real-time Frequency | 
 | Result display ( | Error
100/2000 | 100.04/2000.80 | 0.04 %
120/2400 | 120.02/2400.38 | 0.02 %
150/2600 | 150.15/3003.00 | 0.06 %
Input frequency/Input Speed (F/S) | Real-time Frequency | 
100/2000 | 100.04/2000.80 | 0.04 %
120/2400 | 120.02/2400.38 | 0.02 %
150/2600 | 150.15/3003.00 | 0.06 %

## Slide 20
SIMULATION AND RESULTS
Real-time Frequency case:
F: Input Frequency (Hz).
(RPM), P = 3: number of pole pairs
: measured frequency in fixed case
(RPM)
: error when measuring in fixed case

## Slide 21
Input frequency/Input Speed (F/S) | Real-time Frequency | 
 | Result display ( | Error
150/3000 | 150.24/3004.81 | 0.13%
220/4400 | 220.07/4401.41 | 0.03%
300/6000 | 300.48/6009.62 | 0.009%
Input frequency/Input Speed (F/S) | Real-time Frequency | 
150/3000 | 150.24/3004.81 | 0.13%
220/4400 | 220.07/4401.41 | 0.03%
300/6000 | 300.48/6009.62 | 0.009%